## Slide 1
RythuMitra AI
Smart Irrigation and AI Crop Doctor
An intelligent farming assistance system for sustainable agriculture
Presented by
2500040187 – R.A.E.N Manogna
2510040112 – B. Thanu Sree
2510040043 – M. Sravani
2510040091 – G. Vaishnavi
Department of Electronics and Communication Engineering
KLH University

## Slide 2
Problem Statement
Irrigation
Excessive or insufficient irrigation affects crop growth.
Guidance
Farmers need timely advice on soil conditions and crop problems.
Monitoring
Water usage is hard to track without suitable measurements.
Information
Farming and market information can be hard to access.
Our Goal: An affordable, technology-based farming assistant that supports irrigation monitoring and provides agricultural guidance.

## Slide 3
Proposed Solution
What is RythuMitra AI? A smart farming assistance prototype combining hardware, software and AI-based guidance.
1
Soil moisture monitoring (Arduino + sensor)
2
Auto irrigation-request logic with safety timeout
3
AI-powered agricultural assistance
4
Crop symptom guidance
5
Weather information and farm dashboard
6
Water-flow monitoring capability

## Slide 4
Hardware Components
Arduino Uno: Processes sensor readings and controls the LEDs.
Soil Moisture Sensor (YL-69): Measures soil electrical response to estimate moisture.
Red and Yellow LEDs: Indicate the irrigation status.
Water Flow Sensor: Intended to measure water flow through a pipe.
Breadboard, Resistors, Jumpers: Support circuit connections.
Working Principle
The soil sensor gives an analog reading to the Arduino, which processes it and updates the irrigation status.
Note: The pump is not connected. Water-flow measurements are demo data in the current prototype.

## Slide 5
Working of Smart Irrigation
1
Sensor reads soil condition
2
Arduino averages 10 readings
3
Reading ≥ 450 → dry, irrigation request raised
4
Reading ≤ 400 → wet, request cleared
5
30-second safety timeout stops simulated request
6
Readings and status shown on dashboard
LED Indication
Yellow: request ON
Red: request OFF
The timeout stops the simulated request; it does not control a physical pump in the current setup.

## Slide 6
Software and AI Features
Live Sensor Monitoring
Arduino soil readings and irrigation status.
AI Farmer Assistant
Qwen 2.5 3B model through Ollama.
Crop Doctor
Guidance from symptoms the user describes.
Weather Information
Open-Meteo service when internet is available.
FairPrice Calculator
Price calculation from entered or sample values.
Water Usage Display
Place to demonstrate water-flow information.
One dashboard brings important farming information together in one interface.
AI replies, market prices and water-flow values remain demo data where indicated in the current prototype.

## Slide 7
System Architecture
Hardware Layer
Soil sensor • Arduino Uno • LEDs
▼
Data Processing Layer
Analog readings • Averaging and thresholds • Serial communication
▼
Software Layer
Python Arduino bridge • Web dashboard • Local AI server (Ollama)
▼
User Interface
Soil status • Irrigation request • AI assistance • Weather and farming tools
The Arduino supplies sensor data to the software; the dashboard presents it in a user-friendly format.

## Slide 8
Integration of ECE Subjects
1. Signal Processing
Sampling soil sensor readings
Averaging 10 readings to smooth fluctuations
Pulse counting: intended for water-flow measurement
2. ML and AI
Qwen 2.5 3B gives AI farming guidance
Irrigation decision is threshold-based, not a trained ML model
Crop-disease image classification not implemented
3. AECD
Analog sensor interfacing with Arduino
Voltage signals and analog-to-digital conversion
LED circuits using resistors and digital output pins
Electronics, signal processing and AI software working together in an agricultural application.

## Slide 9
Advantages and Applications
Benefits
Supports monitoring of soil conditions
Clear indication of irrigation requests
Safety timeout in the irrigation logic
Agricultural information via an AI assistant
Hardware readings and software tools in one dashboard
Extendable with real water-flow measurement and pump control
Applications
Small farms and home gardens
Educational smart-agriculture demos
Water-use monitoring systems
Future precision-irrigation solutions

## Slide 10
Conclusion and Future Scope
RythuMitra AI demonstrates soil sensing, Arduino-based irrigation logic, a web dashboard and AI-powered agricultural assistance, a foundation for accessible, affordable smart farming.
Future Scope
Connect a pump driver and water pump for physical irrigation
Integrate and calibrate the water-flow sensor
Train an ML model for crop-disease classification
Add reliable, verified live market-price data
Improve multilingual voice interaction and offline functionality
Thank You | RythuMitra AI – Smarter Farming, Better Decisions.